## Slide 1: Twin Echo-Enabled Harmonic Generation for Enhanced Coherent Bunching at Short Wavelength
Eugenio Ferrari
25.09.2025

## Slide 2: Outline and contents
Echo Enabled Harmonic Generation (EEHG) for FEL external seeding at short wavelengths
Fresh bunch technique for further extend seeding
Performance and limitations of two cascaded EEHG stages

## Slide 3: Echo Enabled Harmonic Generation
Increasing harmonic content to generate short FEL wavelengths
A first laser generates an energy modulation in electron beam.
A strong chicane creates stripes in the longitudinal phase space.
A second laser imprints an energy modulation.
The second chicane converts the energy modulation into harmonic density modulation.
A1
A2
B1
B2
Image from P.R.R. et al., Nature Photonics 13, 555-561 (2019)

## Slide 4: EEHG bunching equation
Dependence on seeding parameters
A1
A2
B1
B2
Modulation amplitude
Chicane strength
EEHG harmonic number
EEHG scaling
EEHG wavenumber

## Slide 5: How to deal with multi-parameter EEHG bunching
Solving the bunching equation numerically with fixed first seeding stage parameters
One possible approach:
  A1 = 3
  R56(1) = 7 mm
  n = -1, m = (aE - n) / K
  Plot bn,m vs. A2, R56(2)
Example: FLASH-1 at 4 nm
Modulation amplitude
Chicane strength
Very high harmonic up-conversion efficiency
Bunching islands

## Slide 6: Fresh bunch approach
An FEL seeding another FEL
HGHG seeding HGHG
EEHG seeding HGHG

## Slide 7: Two cascaded ECHO stages
aE(final) = 1199
EEHG till hard X-rays?
Notes: TEEHG is in a sense similar to the scheme reported in this paper, where the authors were considering EEHG to the hard-x-rays
But we consider instead very small echo numbers
In out case, we saw that the main degradation effect is the finite size of the seed laser

## Slide 8: Two cascaded ECHO stages
e-beam
RAD1
MOD1
MOD2
DS1
DS2
RAD2
MOD3
DS3
DL
*Seed 1
Seed 2
ECHO-1
Fresh bunch
EEHG seeding EEHG
*Seed1 pulse length is comparable to the e-beam to reduce the effects of temporal jitter
H
T
Notes: Now let’s together follow the journey through the setup shown above of two electron beam slices with length of one seed laser wavelength, located towards the tail and towards the head of the bunch
Shown is the longitudinal phase space (E, phase)

## Slide 9: Two cascaded ECHO stages
e-beam
RAD1
MOD1
MOD2
DS1
DS2
RAD2
MOD3
DS3
DL
*Seed 1
Seed 2
Seed 3
ECHO-1
ECHO-2
Fresh bunch
EEHG seeding EEHG
*Seed1 pulse length is comparable to the e-beam to reduce the effects of temporal jitter
H
T
Twice EEHG? TEEHG!
Notes: After ECHO-2 appears:
And what better achronim? Twice EEHG: TEEHG!

## Slide 10: Two cascaded ECHO stages
Bunching maps, harmonic up-conversion (i.e., shorter wavelengths)
ECHO-1 (λFEL = 7.89 nm)
aE1 = 38 (n = -1, m = 39, λ1 = λ2 = 300 nm)
ECHO-2 (λFEL = 4 nm)
aE2 = 75 (n = -1, m = 2, λ1 = 300 nm, λ2 = 7.89 nm)
Optimum for A3 ~ 0.17
Max. bunching ~ 24%
En. Spread ~ 0.33 MeV
Optimum for A2 ~ 2.7
Max. bunching ~ 10%
En. Spread ~ 0.44 MeV
λFEL = 7.89 nm
λFEL = 4 nm
Notes: Now we have two bunching equations to be optimized.
We fix the final wavelength to 4 nm and here are the possible solutions to achieve that

## Slide 11: Two cascaded ECHO stages
Bunching maps, harmonic down-conversion (i.e., longer wavelengths)
ECHO-1 (λFEL = 3.96 nm)
aE1 = 76 (n = -1, m = 77, λ1 = λ2 = 300 nm)
ECHO-2 (λFEL = 4 nm)
aE2 = 75 (n = -1, m = 1, λ1 = 300 nm, λ2 = 3.96 nm)
Optimum for A3 ~ 0.1
Max. bunching ~ 29%
En. Spread ~ 0.33 MeV
Optimum for A2 ~ 5.1
Max. bunching ~ 7%
En. Spread ~ 0.64 MeV
λFEL = 3.96 nm
λFEL = 4 nm

## Slide 12: Two cascaded ECHO stages
Bunching maps, harmonic down-conversion (i.e., longer wavelengths)
ECHO-1 (λFEL = 3.96 nm)
aE1 = 76 (n = -1, m = 77, λ1 = λ2 = 300 nm)
ECHO-2 (λFEL = 4 nm)
aE2 = 75 (n = -1, m = 1, λ1 = 300 nm, λ2 = 3.96 nm)
Notes: The two ECHOs are very different:
Energy spread
Entrance bunching
Modulation amplitude

## Slide 13: Two cascaded ECHO stages
Comparison between harmonic up- and down-conversion
ECHO-2 (λFEL = 4 nm)
down-conversion
aE2 = 75
n = -1, m = 1,
λ1 = 300 nm, λ2 = 3.96 nm
Optimum for A3 ~ 0.1
Max. bunching ~ 29%
ECHO-2 (λFEL = 4 nm)
up-conversion
aE1 = 75
n = -1, m = 2,
λ1 = 300 nm, λ2 = 7.89 nm
Optimum for A3 ~ 0.17
Max. bunching ~ 24%
In both cases:
Very high bunching at 4 nm (>20%)
With tiny modulation amplitude A3
Minute seed3 power requirements:
  Few 104 W peak power*
  ~nJ pulse energy
  Emitted by a single radiator module (and even requiring attenuation)
  RAD1 can be very compact
Small induced energy spread at RAD2
  Practically only determined by A1
Harmonic down-conversion provides the best performance
Achievable bunching is independent on the final wavelength if sufficient seed3 power is available
*For the presented parameters
λFEL = 4 nm
λFEL = 4 nm
Notes: And the simple explanation on why m = 1 is more efficient than m = 2

## Slide 14: Two cascaded ECHO stages
Simulations, down-conversion
Genesis1.3v4 time-independent
ECHO-2 (λFEL = 4 nm)
aE2 = 75 (n = -1, m = 1, λ1 = 300 nm, λ2 = 3.96 nm)
Consequence of the “finite size” of seed3
Can be mitigated:
by longer drift
appropriate e-beam optics
Using small A!
λFEL = 4 nm
Notes: Let’s focus now on the comparison between the model and time independent Genesis simulations
Same number of undulators as source, but different source position (and attenuation to always have A3 = 0.1)

## Slide 15: Two cascaded ECHO stages
Performance comparison
Genesis1.3v4 time-dependent
(λFEL = 4 nm)
* best case scenario: ECHO-1 on 500 A slice, FB on 500 A
** worst case scenario: seed3 from one cell with one cell drift only
Notes: Full fledged time dependent Genesis simulations at 4 nm

## Slide 16: Harmonic social distancing
Cascaded schemes “reset” the harmonic separation
Both setups optimized for 4 nm
The bunching spectrum is show, without altering the tuning

## Slide 17: Two cascaded ECHO stages
aE(final) = 1199
ISR in bending
SR in undulators
Finite size of the laser
Limiting effects:
EEHG till hard X-rays?
IBS
Notes: TEEHG is in a sense similar to the scheme reported in this paper, where the authors were considering EEHG to the hard-x-rays
But we consider instead very small echo numbers
In out case, we saw that the main degradation effect is the finite size of the seed laser

## Slide 18: Amplification of small signals
HHG as seed for EEHG
Seed laser
A1 = 3
HHG source
A2 ~ 0.1
(n = -1, m = 1)
  Few 104 W peak power*
  ~nJ pulse energy
*For our parameters
An alternative to self-modulation, with the reduced sensitivity to e-beam parameters of EEHG
Notes: A somewhat simplified similar to the one shown could be then considered to amplify instead small signals
Like the harmonics in gas

## Slide 19: Summary
EEHG is a well-established external seeding technique for reaching short wavelengths in a single stage
The fresh bunch technique can be used in stages to further extend external seeding
TEEHG is a promising approach to reach high bunching at very short wavelengths
We plan to test the setup soon

## Slide 20: Thank you!

## Slide 21
Eugenio Ferrari
MPY
eugenio.ferrari@desy.de

## Slide 22: Backup

## Slide 23: Dependence on EEHG paramerters

## Slide 24: Controlling seed3 power (A3)
Attenuate ECHO-1 output
Laser heater shaping
Detune of RAD1 or MOD3, tune of ECHO-1 parameters
Solid or gas attenuator for RAD1 emission
  Or a mono?
Current distribution of the beam
  Naturally present
  Conveniently located for FB
Energy
Time

## Slide 25: Dependency on A1
For ECHO-2, fixed R56,1
Even larger bunching is possible, but at the cost of increasing the energy spread.
Next step: optimization of A1 for best performance

## Slide 26: Dependency on m
Higher harmonics

## Slide 27: How to use two empty cells

## Slide 28: Two empty cells
Space for two chicanes!
Shift of the source point towards the users
  This can be critical at long wavelengths
  Transport only an energy modulation to avoid
    space charge effects
Reduce the pulse duration using superradiance
3 Planar Radiators
6 Apple III Radiators
Mod1
Mod2
Chic 1
Chic 2
Chic 0
Notes: Shift of the source position
Superradiant cascades

## Slide 29: Two empty cells
Space for two chicanes!
Militarize* multicolor emission in EEHG:
  One or multiple pulses from from seed2
  Tweak EEHG optimum using the chicanes
3 Planar Radiators
6 Apple III Radiators
Mod1
Mod2
Chic 1
Chic 2
Chic 0
*but still, #makelovenotwar
Color 2: ~8 nm
(n = -1, m = 38, aE = 37)
Color 1: 6 nm
(n = -1, m = 51, aE = 50)
Notes: And finally chicanes can enable cascaded schemes

## Slide 30: FERMI

## Slide 31: FERMI-FEL2
TEEHG for the upgrade of FERMI
Parameter | Value
Energy | 1.8 GeV
Energy spread | 200 keV
Emittance | 0.8 mm mrad
Current | 1 kA
Average beta | 10 m
Radiator | 6 x 2.4 m (λu=29 mm)
Seed λ | 266 nm
TEEHG:
ECHO-1 at 1.98 nm with aE1 = 134 (n = -1, m = 135, λ1 = λ2 = 266 nm)
ECHO-2 at 2 nm with aE2 = 133 (n = -1, m = 1, λ1 = 266 nm, λ2 = 1.98 nm)
Optimum for A3 = 0.093 with bunching ~28%
Preliminary Genesis1.3 simulations with mock-up lattice
*with cubic taper
Notes: I explored what could be the TEEHG performance for the parameters of FERMI FEL-2 upgrade, taken from the CDR
With a mock-up setup, to generate 2 nm radiation in upconversion
Bunching spectrum shown for 1 nm too

## Slide 32: Small signals

## Slide 33: HHG for seeding
Direct amplification and CHG with HHG
Notes: Finally, let’s step back and consider seeding with harmonics in Gas.
This has been demonstrated at long wavelengths, around 160 nm in direct seeding
And at FLASH in CHG mode at 38 and 19 nm
The performance were limited by the amount of power at the harmonics, as this needed to be larger than the energy spread of the electrons (A~1)

## Slide 34: Amplification of small signals
HHG as seed for EEHG
Seed laser
A1 = 3
HHG source
A2 ~ 0.1
(n = -1, m = 1)
  Few 104 W peak power*
  ~nJ pulse energy
*For our parameters
An alternative to self-modulation, with the reduced sensitivity to e-beam parameters of EEHG
Notes: A somewhat simplified similar to the one shown could be then considered to amplify instead small signals
Like the harmonics in gas

## Slide 35: Older stuff

## Slide 36: Two cascaded ECHO stages
Performance comparison
Genesis1.3v4 time-dependent
(λFEL = 4 nm)
Taper is critical
For now, only quadratic
Next steps:
detailed taper optimization
Conditions for high extraction efficiency could be satisfied
very high bunching
(possibly) high seed
Notes: The high extraction efficiency could provide energy extraction up to %-level of the beam power

## Slide 37: Foreword
Once upon a time…
there was an FEL facility going through an upgrade for realizing seeding at high repetition rates.
A dangerous dragon called “Budget Constraints” threatened to filibuster the project.
And this is how the story begins…

## Slide 38: Seeding FLASH1
Modifications to FLASH facility for external seeding
RF Stations
5 MeV
150 MeV
1350 MeV
Bunch Compressors
550 MeV
Accelerating Structures
Lasers
RF Gun
Photon Diag.
TDS
FLASH1
FLASH2
Albert Einstein
Kai Siegbahn
FLASHForward
FEL Experiments
Laser Heater
Seed Laser
FF Laser
THz
Pump-Probe Lasers
Seeding
Energy
Time
Typical phase space for seeding:
500 pC / 1 ps / 500 A Gaussian
 | Seeded FLASH1
Wavelength (nm) | 4 – 60
Photon energy (eV) | 310 – 20.6
Rel. fwhm bandwidth (%) | 0.05 – 0.4
Pulse energy (mJ) | < 20
Pulse energy stability (%) | < 10
Pulse length (fs) | 12 - 40
Pulses per second | < 5000
Polarization | Variable (linear to circular)
Parameter | Value
Energy | 1.35 GeV
Energy spread | 150 keV
Emittance | 0.6 mm mrad
Current | 500 A
Average beta | 10 m
Seed λ | 343 nm / 297 - 317 nm 300 nm*

## Slide 39: Seeding FLASH1
The “infinite money approximation” doesn’t hold
SASE saturation
11x Apple III
6x Apple III
11 Radiators
Mod1
Mod2
Chic 1
Chic 2
Chic 0
← Output power reduced by a factor of 5
← Polarization contrast reduced to about 50
→ SASE is no fallback option
→ 24/7 operation of seed laser!
Reduce performance
Maintain upgrade capability
Upgrade to full version when budget becomes available
3 Planar Radiators
6 Apple III Radiators
Mod1
Mod2
Chic 1
Chic 2
Chic 0
But there are still two empty radiator cells
Notes: E = 1350 MeV
I = 2 kA
Espread = 600 keV (150 keV@500 A)
Av. Beam size = 50 um
Norm. Emittance = 0.6 mm mrad
Average beta function = 10 m

## Slide 40: Better a chicane today than an undulator tomorrow?
(Almost) anything is better than a drift*
Chicanes are great for flexibility
  Adapt the source position
  Multicolor pulses, pulse shortening, cascades
  and for thinking outside the box
  and they are cheaper
Undulators are better for (increased) output power
TEEHG is a promising approach to reach unprecedented bunching at very short wavelengths
Can we have both?
Notes: Maybe a clever design, similar to what presented yesterday by Shaukat, where an undulator could be quickly swapped into a chicane