## Slide 1: 5D Phase space reconstruction at DESY and PSI
Sonja Jaster-Merz, Francesco Demurtas, Paolo Craivich, Philipp Dijkstal et al.
philipp.dijkstal@psi.ch, 25 September 2025
FELs of Europe topical workshop on selected problems in FEL physics: from soft X-rays to THz

## Slide 2: Content
General information on PolariX TDS project
The 5D reconstruction method
Results from FLASHForward
Preliminary results from SwissFEL

## Slide 3: Polarizable X-band transverse deflection structure (TDS)
PolariX enables new diagnostic methods and allows for sub-fs longitudinal resolution
Designed in collaboration between CERN, PSI and DESY [13-15].
Installed at: FLASH 2, FLASHForward, ARES, SwissFEL.
Sub-fs resolution possible.
Unique feature: Variable streaking angle.
PolariX TDS installed at the ARES linac.

## Slide 4: Motivation
References:
A. Grudiev, CLIC-Note-1067 (2016)
P. Craievich et al., Phys. Rev. Accel. Beams 23, 112001 (2020)
B. Marchetti et al., Sci Rep 11, 3560 (2021)
P. González Caminal et al., Phys. Rev. Accel. Beams 27, 032801 (2024)
Diagnose multidimensional phase space of electron bunches to investigate complex beam dynamics (e.g. collective effects, beam correlations, slice emittance in different planes, etc..)
  5D/6D phase-space characterization becomes possible by different streaking planes and using tomographic methods.
  Reconstruction of the 3D charge density.
POLARIzable X-band Transverse Deflection Structure – POLARIX TDS

## Slide 5: Method to achieve variable polarization
POLARIzable X-band Transverse Deflection Structure – POLARIX TDS
Variable polarization circular TE11 mode launcher: E-rotator
DESY-CERN-PSI Collaboration
1x TDS FLASHForward (DESY)
2x TDS FLASH II (DESY)
2x TDS SINBAD-ARES (DESY)
2x TDS SwissFEL Athos (PSI)
Phase difference between port 1 and port 2:
0 degree -> vertical polarization
180 degree -> horizontal polarization

## Slide 6: PolariX TDS and RF components at PSI
All waveguide RF components including the XBOC, and phase shifters were designed and built at PSI, X-Band Klystron is a CPI VKX-8311A, 50 MW (max used rf power 35 MW). PSI HV klystron modulator: developed and built in-house (400 kV, 3 ms). deflecting voltage ~90 MV.
XBOC (PSI)
RF loads
3 Phase shifter (PSI)
E. Prat et al., Advanced Photonics 7 (2), 026002 (2025)
Rms resolution down to ~300 attoseconds in low charge (i.e. low emittance) beam configuration has been demonstrated.
Main use case: measurement of current / FEL power profiles during machine setup or special mode development.

## Slide 7: 5D phase-space tomography – method[1-4]
Reconstructing the full transverse phase-space of each longitudinal slice
[1] S. Jaster-Merz et al., Phys. Rev. Accel. Beams 27, 072801, 2024 - METHOD
[2] S. Jaster-Merz et al., https://doi.org/10.48550/arXiv.2505.13724, PROOF of PRINCIPLE
[3] S. Jaster-Merz et al ., LINAC2022, MOPORI10, 2022,
[4] S. Jaster-Merz et al ., IPAC2022, MOPOPT021, 2022
[5] K. Hock and A. Wolski, Nucl. Instrum. Methods Phys. Res. Sect. A, 2013
[6] D. Marx et al., Journal of Physics: Conference Series, vol. 874, 2017
[5]
[6]
Two independent rotations, via transverse optics (θₓ, θy) and TDS streak angles, enable mapping from 2D images to full 5D distribution.
Hierarchical reconstruction: first resolve (x, y, t), then expand each time slice into full transverse phase space.
Resolution and accuracy are tunable via beamline tuning (β-matching), TDS voltage, drift length, and number of projections.
Only drift space between TDS and screen.

## Slide 8: Excellent performance demonstrated in simulations
Full 5D reconstruction of Gaussian and highly complex phase spaces.
Beam parameters reconstructed with ≲ 5% discrepancies.
Extraction of sliced beam parameters and the 4D slice emittance possible.
Proof-of-principle simulation studies with test distributions using the ARES beamline
Visualization done with PyVista
beam charge: 1 pC
beam energy: 155 MeV
S. Jaster-Merz et al., Phys. Rev. Accel. Beams 27, 072801 (2024)

## Slide 9: Experimental demonstration at FLASHForward
Fully commissioned PolariX TDS and flexible diagnostic beamline available
Experimental facility dedicated to beam driven plasma acceleration experiments.
Uses up to 1.3 GeV electron beams from the FLASH linac.
Measurement performed with 10 Hz single bunch operation, ~1.1 GeV energy, ~0.3 nC charge, and ~200 fs RMS bunch duration.
S. Jaster-Merz et al., https://doi.org/10.48550/arXiv.2505.13724

## Slide 10: First experimental 5D reconstruction
Feasibility of conducting a 5D tomography measurement is demonstrated for the first time
Visualization done with PyVista
head
tail
beam charge: 300 pC
Average longitudinal resolution of 20 fs.
Reconstruction of 72 bins in the longitudinal plane and 301 bins (3.3 µm/√m) per transverse plane.
960 projections recorded in ~28 hours.
3D projection (x’N, y’N, t)
S. Jaster-Merz et al., https://doi.org/10.48550/arXiv.2505.13724

## Slide 11: Reconstructed 5D phase space enables new insights
Previously hidden transverse-longitudinal correlations are retrieved
‌‌All 2D projections of the 5D phase space obtained from the reconstruction.
Transverse phase space reconstruction validated against dedicated 4D tomography measurement.
S. Jaster-Merz et al., https://doi.org/10.48550/arXiv.2505.13724

## Slide 12: Extraction of sliced beam parameters from reconstruction
In addition to the full 5D phase space distribution the reconstruction allows to obtain:
  ‌Sliced transverse beam parameters,
  ‌Bunch duration and current profile,
  Sliced 4D emittance.
  Projected transverse beam parameters.
Information about both transverse planes can be obtained simultaneously
Projected quantities validated against multi-quadrupole scan and TDS bunch duration measurements.
S. Jaster-Merz et al., https://doi.org/10.48550/arXiv.2505.13724

## Slide 13: 5D measurement optics preparation
To perform the 5D tomography the 3D reconstruction must be combined with a quadrupole scan in both x and y planes
TDS 1
TDS 2
DSCR120
Reconstruction Point
from 96 to 236 in ten steps 100 quadrupole settings

## Slide 14: 5D tomography method successfully applied at PSI
Two 5D datasets for different beam settings were recorded
Beam 1: Compressed ~56 fs short (FWHM)
Beam 2: Reduced beam tilts, ~103 fs (FWHM)
Preliminary results.
Preliminary results.
For each dataset, we acquired 5 images for each combination of 100 quadrupole settings and 10 polarizations (+unstreaked case) in about 7 hours.
Beam repetition rate: 1 Hz.

## Slide 15: 5D Reconstruction: Calibration results
TDS calibration for different streaking angles Measured the centroid shift when changing the cavity phase.
Low variation in the calibration factors for different streaking angles, as expected.
Average resolution rescaled to take into account shot-to-shot variations in the cavity voltage.

## Slide 16: 2D projections of the reconstructed phase space of beam 1
Reconstructed 5D distribution reveals beam tilts
Preliminary results.

## Slide 17: Reconstruction of beam 2
Relaxing the compression reduced tilts
Preliminary results.

## Slide 18: Outlook: PolariX at ARES
Designed to produce and characterize bunches of high quality with sub-fs duration.
Applications using sub-pC charge beams.
Drive towards high-precision longitudinal diagnostics, detailed phase-space characterization, and highly sensitive diagnostic tools.
https://ares.desy.de/
Accelerator test facility for novel diagnostics, advanced acceleration schemes, medical applications, …

## Slide 19: PolariX setup at ARES
Located downstream of first experimental chamber and bunch compressor.
Two PolariX TDSs with independent RF supply.
2 x 6 MW CPI klystrons + 2 BOCs.
Expected longitudinal resolution: ~0.2 fs assuming 20 MV peak voltage for each TDS.
Commissioning is ongoing, and first 3D phase space reconstructions were performed.

## Slide 20: Summary and outlook
The first X-band TDS with variable polarization was designed, built, and tested in a joint project between CERN, DESY and PSI.
The variable polarization allows to directly measure various kinds of phase space correlations.
The 5D reconstruction method was successfully demonstrated at 2 facilities (SwissFEL and FLASH), with ARES results expected for 2026.
Disadvantage: long measurement times. Prohibitive for FEL user facilities (except in special machine study time)!
Measurements with the PolariX TDS should be combined with generative machine learning techniques, as demonstrated for example in R. Roussel et al., Phys. Rev. Accel. Beams 27, 094601 (2024).

## Slide 21: Aknowledgments
S. Jaster-Merz, B. Beutner, R. W. Assmann, J. Beinortaitė, J. Björklund Svensson, R. Brinkmann, F. Burkart, H. Dinter, P. González Caminal, W. Hillert, A. L. Kanekar, M. Kellermeier, W. Kuropka, F. Mayet, J. Osterhoff, B. Stacey, M. Stanitzki, T. Vinatier, S. Wesch, R. D’Arcy (DESY)
Francesco Demurtas, Enrica Chiadroni, Anna Giribono (INFN)
P. Craievich, F. Marcellini, E. Prat, S. Reiche, Z. Geng, E. Ericson, R. Ischebeck (PSI)
PSI , Areal view