## Slide 1
Pulse to Pulse stability
Kévin Pepitone
LLRF Topical Workshop on Advanced Feedback Control
13-15 October 2026, Nova Gorica, Slovenia

## Slide 2
How to measure it?
What is the impact?
What is the pulse-to-pulse stability?
Table of content
K-series
Splitcore™
Pulse Transformer
Pulse to Pulse Control™
CCPS
Parallel Switching™
Switch Units
ScandiCAT™
Control Systems
Integrated Klystron and Solenoid
K300 RF Unit

## Slide 3
Pulse to pulse stability
Definition
Pulse to Pulse Stability: Consistency of energy or particle pulses from one pulse to the next.
Why Does It Matter for Accelerators & LLRF?
RF Phase & Amplitude Jitter: High-voltage fluctuations directly translate into phase jitter at the klystron output.
Beam Synchronization & Emittance: In modern linacs and FELs, phase errors degrade arrival-time stability, bunch compression, and longitudinal emittance.

## Slide 4
Definition of a klystron
Phase stability of the pulse modulator
A klystron is an electron source in which electron are produced, accelerated and dumped in a very short distance
The modulator produces the electric field to accelerate the electrons between the anode and the cathode
The klystron consists of a cylindrical vacuum chamber containing a series of electrodes that accelerate and decelerate the electron beam, creating oscillations at a desired frequency

## Slide 5
Theory
Phase stability of the pulse modulator
where is the accelerating voltage, is the electron charge and is the rest energy
where is the Lorentz factor which is
We obtain that the electron velocity and finally the traveling time of the electrons on the tube which is
The phase depends on the traveling time by
A small variation the accelerating voltage will imply a small variation on the traveling time which implies a small variation on the phase

## Slide 6
From Pulse to pulse to Phase stability
Phase stability of the pulse modulator
By computing the previous equations, we obtain that
  The traveling time is 2.60057 ns
Pulse to pulse stability (ppm) | Voltage difference (V) | Traveling time (ns) | Traveling time difference (ps) | Phase stability (°)
1000 | 155.00 | 2.59971 | 0.8655 | 0.9348
500 | 77.50 | 2.60014 | 0.4330 | 0.4676
200 | 31.00 | 2.60040 | 0.1732 | 0.1871
100 | 15.50 | 2.60049 | 0.0866 | 0.0936
70 | 10.85 | 2.60051 | 0.0606 | 0.0655
10 | 1.55 | 2.60056 | 0.0087 | 0.0094
8 | 1.24 | 2.60057 | 0.0069 | 0.0075
Let’s consider a driving voltage = 155 kV, which has a traveling tube of = 0.5 m and operates at a constant temperature and at = 3 GHz
Now let’s consider variation of the driving voltage

## Slide 7
Comparison of 3 klystrons
Phase stability of the pulse modulator
Klystron | Pulse to pulse stability (ppm) | Voltage difference (V) | Traveling time (ns) | Traveling time difference (ps) | Phase stability (°)
TH2100 | 50 | 15.35 | 2.18281 | 0.0262 | 0.028
E37202 | 50 | 18.00 | 1.85353 | 0.0201 | 0.041
VKX8311A | 50 | 20.50 | 3.18741 | 0.0316 | 0.136
TH2100
50 MW
S-band
2998 MHZ
307 kV
0,51 m tube
2.18283 ns
E37202
50 MW
C-band
5712 MHZ
360 kV
0,45 m tube
ns
VKX8311A
50 MW
X-band
11994 MHZ
410 kV
0,795 m tube
3.18744 ns
K400
RF peak power: 30 – 60 MW
Pulse voltage: 280 – 450 kV
Pulse current: 230 – 450 A
Modulator peak: 160 MW
Modulator avg.: 125 kW

## Slide 8
What Else Impacts Klystron Phase?
Power supplies drift:
  Solenoid current () sets axial field and controls beam radius ().
  Alters bunching distance (): the electron bunch centroid shifts relative to the catcher cavity gap.
  Typical phase drift from the solenoid: 0.5° to 2.5° per 1%
  Heater voltage drift modulates cathode temperature and shifts the gun perveance ():
  Radial thermal gradients alter the effective emitting area
  Axial thermal expansion of the cathode support modulates the cathode-anode gap
  Beam current and plasma frequency , shifting the RF bunch centroid arrival time
Beyond High Voltage

## Slide 9
Measurements
Beyond High Voltage
Power supplies were measured over a shunt.
The stability is given as the sdev of the drop voltage over the shunt normalized by the mean coil voltage (this is shunt dependent)
Device | Typical stability (ppm) | Estimated phase contribution (°)
Solenoids | 10-50 ppm | 0.0005 – 0.0125
Heater | 10-20 ppm | -

## Slide 10
What Else Impacts Klystron Phase?
Thermal Drift & Cavity Detuning:
  Cavity resonant frequency shifts with copper thermal expansion (≈ 16.5 ppm/K)
  Phase variation around resonance:
  For , a temperature fluctuation of
  yields
  Stringent cooling water stability is mandatory, slow process
Beyond High Voltage

## Slide 11
AM/PM Conversion
Non-linear Electron Bunching:
  Low drive (small-signal regime): Output RF phase is drive-independent ().
  Near / at saturation: Space-charge repulsion and over-bunching alter electron trajectories; the temporal centroid of the bunch shifts upon arrival at the catcher cavity gap.
AM-to-PM Conversion Coefficient ():
Any amplitude noise from the RF driver (SSPA) converts into output phase jitter:
Typical values for high-power pulsed klystrons is 1° to 4° / dB
Klystron Saturation

## Slide 12
Closed-Loop Turnkey RF Unit
LLRF as an Ultra-Fast High-Voltage Diagnostic Tool
Collaboration

## Slide 13
Closed loop
RF layout

## Slide 14
Experimental measurements
Advantages
100 pulses at 3.1 MW, 3.5 μs and 50 Hz measured over 1 μs
The modulator contributes up to
8.6 m RMS on the phase stability

## Slide 15
Application
Klystrons theory
A phase variation of 8.6 m(8.0 fs) will correspond to a pulse-to-pulse
stability of 8.0 ppm
If we consider the klystron having m and a modulator voltage of kV

## Slide 16
Conclusions
Direct HV-to-Phase Link:
Modulator stability sets the RF phase noise floor — modern solid-state modulators (ScandiNova K-series) reach approx 0.01° in S-band.
Frequency Scaling Matters:
The same HV stability yields 4× more phase jitter at X-band than at S-band — higher frequencies demand tighter HV control.
Modulator & LLRF Synergy:
A stable modulator frees the LLRF loop to focus on cavity/beam-loading regulation instead of correcting HV imperfections.
Takeaways

## Slide 17
Thanks for your attention!